## Slide 1: Binære Tællere
Gerth Stølting Brodal (Aarhus Universitet)
Mark Greve (Aarhus Universitet)
Vineet Pandey (BITS Pilani, Indien)
S. Srinivasa Rao (Seoul, Syd Korea)
Verdens Kedeligste Foredrag, Tågekammeret, Aarhus Universitet, 2. marts 2011
Notes: 20 min oplæg

## Slide 3: 0

## Slide 4: 1

## Slide 5: 10

## Slide 6: 11

## Slide 7: 100

## Slide 8: 101

## Slide 9: 110

## Slide 10: 111

## Slide 11: 1000

## Slide 12: 1001

## Slide 13: 1010

## Slide 14: 1011

## Slide 15: 1100

## Slide 16: 1101

## Slide 17: 1110

## Slide 18: 1111

## Slide 19: 0000
- vi tæller modulo 100002 = 1610

## Slide 20: 1011
1∙23+ 0∙22+ 1∙21+ 1∙20 = 8+2+1 = 1110

## Slide 21
Decimal | Binær
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111
0 | 0000
b3b2b1b0
b0
0 1
b1
b2
b3
0 1
0 1
0 1
---1
--10
0000
-100
1000
læser 4 bits
skriver 4 bits
Decimal | Binær
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111
0 | 0000
Decimal | Binær
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111
0 | 0000
Algoritme

## Slide 22
Recovering..........

## Slide 23
Decimal | Binær | Spejlet Gray kode | 
0 | 0000 | 0000 | 
1 | 0001 | 0001 | 
2 | 0010 | 0011 | 
3 | 0011 | 0010 | 
4 | 0100 | 0110 | 
5 | 0101 | 0111 | 
6 | 0110 | 0101 | 
7 | 0111 | 0100 | 
8 | 1000 | 1100 | 
9 | 1001 | 1101 | 
10 | 1010 | 1111 | 
11 | 1011 | 1110 | 
12 | 1100 | 1010 | 
13 | 1101 | 1011 | 
14 | 1110 | 1001 | 
15 | 1111 | 1000 | 
0 | 0000 | 0000 | 
"To get the next code, for a code with even parity, flip the rightmost bit. For a code with odd parity, find the rightmost ‘1’ and flip the bit to its left. The only special case is when the last bit bn is the only ‘1’ in the code. This is also the last code in the sequence."
Decimal | Binær | Spejlet Gray kode | 
0 | 0000 | 0000 | 
1 | 0001 | 0001 | 
2 | 0010 | 0011 | 
3 | 0011 | 0010 | 
4 | 0100 | 0110 | 
5 | 0101 | 0111 | 
6 | 0110 | 0101 | 
7 | 0111 | 0100 | 
8 | 1000 | 1100 | 
9 | 1001 | 1101 | 
10 | 1010 | 1111 | 
11 | 1011 | 1110 | 
12 | 1100 | 1010 | 
13 | 1101 | 1011 | 
14 | 1110 | 1001 | 
15 | 1111 | 1000 | 
0 | 0000 | 0000 | 
læser altid 4 bits
skriver altid 1 bit
---0
b0
b1
b2
--1-
---0
---0
--0-
--0-
--1-
-0--
b2
b2
b2
b1
0 1
0 1
0 1
0 1
0 1
0 1
0 1
0---
---1
-1--
1---
---1
---1
---1
----0
b3
0 1
b3
0 1
b3
0 1
b3
0 1
b3
0 1
b3
0 1
b3
0 1
b3
0 1
b3b2b1b0

## Slide 24
Notes: Wikipedia:
Reflected binary codes were applied to mathematical puzzles before they became known to engineers. The French engineer Émile Baudot used Gray codes in telegraphy in 1878. He received the French Legion of Honor medal for his work. The Gray code is sometimes attributed, incorrectly,[5] to Elisha Gray (in Principles of Pulse Code Modulation, K. W. Cattermole,[6] for example).
Frank Gray, who became famous for inventing the signaling method that came to be used for compatible color television, invented a method to convert analog signals to reflected binary code groups using vacuum tube-based apparatus. The method and apparatus were patented in 1953 and the name of Gray stuck to the codes. The "PCM tube" apparatus that Gray patented was made by Raymond W. Sears of Bell Labs, working with Gray and William M. Goodall, who credited Gray for the idea of the reflected binary code.
Part of front page of Gray's patent, showing PCM tube (10) with reflected binary code in plate (15)
The use of his eponymous codes that Gray was most interested in was to minimize the effect of error in the conversion of analog signals to digital; his codes are still used today for this purpose, and others.

## Slide 26
Spørgsmål
Kan man lave en binær tæller hvor man aldrig behøver at kigge på alle bit for at tælle op?

## Slide 27
Decimal | 
0 | 0000
1 | 0001
2 | 0100
3 | 0101
4 | 1101
5 | 1001
6 | 1100
7 | 1110
8 | 0110
9 | 0111
10 | 1111
11 | 1011
12 | 1000
13 | 1010
14 | 0010
15 | 0011
0 | 0000
Decimal | 
0 | 0000
1 | 0001
2 | 0100
3 | 0101
4 | 1101
5 | 1001
6 | 1100
7 | 1110
8 | 0110
9 | 0111
10 | 1111
11 | 1011
12 | 1000
13 | 1010
14 | 0010
15 | 0011
0 | 0000
Decimal | 
0 | 0000
1 | 0001
2 | 0100
3 | 0101
4 | 1101
5 | 1001
6 | 1100
7 | 1110
8 | 0110
9 | 0111
10 | 1111
11 | 1011
12 | 1000
13 | 1010
14 | 0010
15 | 0011
0 | 0000
b3b2b1b0
-1-0
b0
b1
b1
---1
--1-
---1
0---
--00
1---
-0--
b3
b3
b3
b2
0 1
0 1
0 1
0 1
0 1
0 1
0 1
læser altid 3 bits
skriver altid ≤ 2 bits
[B., Greve , Pandey, Rao 2011]

## Slide 28
bn-1 bn-2 ∙∙∙ b6 b5 b4 b3 b2 b1 b0
Generalisering til tællere med n bit
Y
4 bit
3 læsninger
2 skrivninger
X
n-4 bit Gray kode
n-4 læsninger
1 skrivning
metode Increment(XY)
inc(X)
if (X == 0) inc(Y)
læser altid n-1 bits
skriver altid ≤ 3 bits
[B., Greve , Pandey, Rao 2011]

## Slide 29
Sætning
4-bit tæller med 3 læsninger og 2 skrivninger
n-bit tæller med n-1 læsninger og 3 skrivninger
Åbne problemer
n-1 læsninger og 2 (eller 1) skrivninger ?
« n læsninger og skrivninger ? [skal mindst læse log2 n]
-1-0
b0
b1
b1
---1
--1-
---1
0---
--00
1---
-0--
b3
b3
b3
b2
0 1
0 1
0 1
0 1
0 1
0 1
0 1
n=5
?
?
bit læst
bit skrevet
Notes: Gray code
Theorem, 2. linie
Box) Brute force disprove

## Slide 30
TAK