## Slide 1: Multi-core Computing Lecture 1 MADALGO Summer School 2012 Algorithms for Modern Parallel and Distributed Models
Phillip B. Gibbons
Intel Labs Pittsburgh
August 20, 2012
Hi-Spade

## Slide 2: Lecture 1 Outline
Multi-cores: today, future trends, challenges
Computations & Schedulers
    Modeling computations in work-depth framework
    Schedulers: Work Stealing & PDF
  Cache miss analysis on 2-level parallel hierarchy
    Private caches OR Shared cache
  Low-depth, cache-oblivious parallel algorithms
    Sorting & Graph algorithms

## Slide 3: 32-core Xeon 7500 Multi-core
up to 1 TB Main Memory
4 …
24MB Shared L3 Cache
2 HW threads
32KB
256KB
2 HW threads
32KB
256KB
8 …
socket
24MB Shared L3 Cache
2 HW threads
32KB
256KB
2 HW threads
32KB
256KB
8 …
socket
Attach: Magnetic Disks & Flash Devices
Notes: 32KB L1 Instruction caches not shown
Nehalem-EX, up to 2.66 GHz, 45nm
4 sockets with one-hop interconnect. 32 cores / 64 hardware threads
Up to 256 sockets / server (but then not all one-hop)

## Slide 4: 48-core AMD Opteron 6100
up to 0.5 TB Main Memory
4 …
12MB Shared L3 Cache
P
64KB
512KB
P
64KB
512KB
12 …
socket
12MB Shared L3 Cache
P
64KB
512KB
P
64KB
512KB
12 …
socket
Notes: 32KB L1 Instruction caches not shown
Nehalem-EX, up to 2.66 GHz, 45nm
4 sockets with one-hop interconnect. 32 cores / 64 hardware threads
Up to 256 sockets / server (but then not all one-hop)

## Slide 5: 96-core IBM z196 Multi-core
196 MB
196 MB
Memory: Up to 3 TB
4 of these
L4
L3
L2
L1
6 of these
24 MB
1.5 MB
1.5 MB
4 of these
128 KB
P
128 KB
P
24 MB
1.5 MB
1.5 MB
4 of these
128 KB
P
128 KB
P
6 of these
24 MB
1.5 MB
1.5 MB
4 of these
128 KB
P
128 KB
P
24 MB
1.5 MB
1.5 MB
4 of these
128 KB
P
128 KB
P
4 levels of cache

## Slide 6: Hierarchy Trends
Good performance [energy] increasingly requires effective use of hierarchy
Hierarchy getting richer
    More cores
    More levels of cache
    New memory/storage technologies
      Flash/SSDs, emerging PCM
      Bridge gaps in hierarchies – can’t just look at last level of hierarchy

## Slide 7: Harder to Use Hierarchy Effectively
Challenges
Cores compete for hierarchy
Hard to reason about parallel performance
Hundred cores coming soon
Cache hierarchy design in flux
Hierarchies differ across platforms
…
…
…

## Slide 8: How Hierarchy is Treated Today
Ignorant
(Pain)-Fully
Aware
Hand-tuned to platform
Effort high, Not portable, Limited sharing scenarios
API view: Memory + I/O;
Parallelism often ignored
Performance iffy
Algorithm Designers & Application/System Developers tend towards one of two extremes
Or they focus on one or a few aspects, but without a comprehensive view of the whole

## Slide 9: Hierarchy-Savvy Sweet Spot
Ignorant
performance
programming effort
Platform 1
Platform 2
Hierarchy-Savvy
Goal: Modest effort, good performance, robust, strong theoretical foundation
(Pain)-Fully
Aware

## Slide 10: Multi-core Computing Lectures: Progress-to-date on Key Open Questions
How to formally model multi-core hierarchies?
What is the Algorithm Designer’s model?
What runtime task scheduler should be used?
What are the new algorithmic techniques?
How do the algorithms perform in practice?

## Slide 11: Focus: Irregular Algorithms
Sequences and strings: Sorting, Suffix arrays, Seq. alignment
Graph algorithms: Min spanning tree, BFS, coloring, separators
Machine learning: Sparse SVM, K-means, Gibbs sampling, LASSO
Graphics: Ray tracing, Micropoly rendering
Geometry: Delaunay triangulation, Nearest neighbors, N-body
Compared to well-studied regular algorithms:
Harder to find effective parallelism
Harder to exploit memory hierarchy

## Slide 12: Lecture 1 Outline
Multi-cores: today, future trends, challenges
Computations & Schedulers
    Modeling computations in work-depth framework
    Schedulers: Work Stealing & PDF
  Cache miss analysis on 2-level parallel hierarchy
    Private caches OR Shared cache
  Low-depth, cache-oblivious parallel algorithms
    Sorting & Graph algorithms

## Slide 13: Coarse- vs. Fine-grain threading
Coarse Threading popular for decades
    Spawn one thread per core at program initialization
    Heavy-weight O.S. threads
    E.g., Splash Benchmark
  Better Alternative:
    System supports user-level light-weight threads
    Programs expose lots of parallelism
    Dynamic parallelism: forking can be data-dependent
    Smart runtime scheduler maps threads to cores, dynamically as computation proceeds
e.g., Cilk++, Intel TBB, OpenMP, MS Parallel Task Library

## Slide 14: PRAM vs. Work-Depth Framework
PRAM [Fortune, Wyllie ‘78]
    P processors, Shared memory, Synchronous
    Algorithm specifies what each processor does at each synchronous step
  Work-Depth framework [Shiloach, Vishkin ‘82]
    Shared memory, Synchronous
    Algorithm specifies what tasks (work) can be done in parallel at each synchronous step
    Work W is number of tasks
    Depth D is number of steps
    Brent’s “Theorem” [‘74]: On P processors, Time ≤ W/P + D

## Slide 15: Work-Depth Generalized to Nested Parallel Computations
Computation DAG:
    Nodes are tasks
    Edges are dependences between tasks
  Work = sequential execution time
  Depth = span = critical path length
Common Assumptions:
Structure may depend on input: revealed online
Nested-parallel (fork/join): DAG is series-parallel
Structure is independent of the parallel schedule

## Slide 16: Example Computation DAGs
O(log n)
O(log2 n)
Quicksort variant
Sum
…
…
…
…
…
…
…
…
…
…
O(log n)
Matrix Multiply

## Slide 17: Sequential Schedule
Any topological sort of the DAG
Example: sequential depth-first schedule
1
2
3
4
5
6
8
7
9
10
11
12
13
Notes: DAG: directed acyclic graph; it is unfolded on-the-fly

## Slide 18: Parallel Schedules
Up to P tasks executed on each time step
1
2
5
6
7
2
3
3
3
4
4
4
8
Greedy Schedule: if there are ready tasks, do them.
Will guarantee:
Time ≤ W/P + D
within a factor of 2 of optimal
Time Step
a 3 processor schedule

## Slide 19: Work Stealing Parallel Scheduler
WS = work stealing as in Cilk, elsewhere
  Forked tasks placed on local work queue
  Processor works from bottom of local queue
  When local queue empty, steal top task from random queue
Bound number of steals using WS
  Thrm: Expected O(P D) steals for nested-parallel DAG of depth D, on P processors [Blumofe, Leiserson '99]
    Proof intuitively shows that every O(P) steals, depth remaining must decrease by ≥1

## Slide 20: Prioritized Schedules & PDF
Among ready nodes, always give priority to earliest in the sequential schedule
1
2
3
4
5
6
7
8
9
10
11
12
13
1
2
3
4
3
4
3
4
5
2
5
6
7
Sequential
1
2
3
4
3
4
5
6
7
2
3
4
8
Not prioritized
(from before)
Prioritized
Parallel Depth-First (PDF) [Blelloch, G, Matias ‘99]: prioritized based on depth-first sequential schedule

## Slide 21: Lecture 1 Outline
Multi-cores: today, future trends, challenges
Computations & Schedulers
    Modeling computations in work-depth framework
    Schedulers: Work Stealing & PDF
  Cache miss analysis on 2-level parallel hierarchy
    Private caches OR Shared cache
  Low-depth, cache-oblivious parallel algorithms
    Sorting & Graph algorithms

## Slide 22: Cache Misses: Simplified Scenarios
Memory
CPU
CPU
Shared Cache
CPU
Memory
CPU
CPU
CPU
Private caches of size M1 each
Shared cache of size Mp
One level of caches, block size = 1
Ideal replacement policy
Memory
CPU
Sequential: cache of size M1
Number of cache misses depends on the schedule
Notes: Condense 9&10 in to one
Mention nested parallelism as necessary for WS, skip the nested parallelism slide
Mention transpose and sorting and contrast their bounds
Note low depth is the important factor here. Cite by name
Show with example (sorting), which term is the dominant one? Qs or pdz?
What does Qp mean?
What does cache complexity mean for the running time?
-- for a greedy scheduler, the relation is “linear”
What we want
-- optimal work, Qs…

## Slide 23: Parallel Schedule with Many Misses
…
Reads same location M1 apart
…
…
…
Repeat n times
Sequential schedule has
  2 M1 misses
Parallel schedule (P=2):
…when Mp = M1 has
  n M1 misses
…when Mp = 2M1 has
  2 M1 misses only
a1
a2
a1
a2
b1
b2
b1
b2
bM1
aM1
Memory
CPU
CPU
Shared Cache
Mp
Memory
CPU
M1

## Slide 24
Parallel Depth First (PDF):
Work Stealing (WS):
Shared cache = 0.5 *(src array size + dest array size).
Cache miss
Cache hit
Mixed
8 cores
Parallel Merge Sort: WS vs. PDF

## Slide 25: WS Cache Bounds
Memory
CPU
CPU
Mp
CPU
Memory
CPU
M1
CPU
M1
CPU
M1
Memory
CPU
M1
Private caches: [Blumofe et al. ’96; Acar, Blelloch, Blumofe ‘02]
  Only O(P D M1) more misses than sequential
    Proof idea: Each of O(PD) steals incurs O(M1) extra misses
    Assumes DAG consistency among caches
Shared Cache:
  Mp = P M1 for no more misses than sequential
(Bounds are tight. D is the worst case running time of critical path)
Notes: Condense 9&10 in to one
Mention nested parallelism as necessary for WS, skip the nested parallelism slide
Mention transpose and sorting and contrast their bounds
Note low depth is the important factor here. Cite by name
Show with example (sorting), which term is the dominant one? Qs or pdz?
What does Qp mean?
What does cache complexity mean for the running time?
-- for a greedy scheduler, the relation is “linear”
What we want
-- optimal work, Qs…

## Slide 26: PDF Cache Bounds
Memory
CPU
CPU
Mp
CPU
Memory
CPU
CPU
CPU
Memory
CPU
M1
Private caches:
  Exercise: How bad can it be?
Shared Cache: [Blelloch, G ’04]
  Only Mp = M1 + P D (vs. Mp = P M1 for WS) for no more misses than sequential
M1
M1
M1
(Bound is tight. D is the worst case running time of critical path)
Notes: Condense 9&10 in to one
Mention nested parallelism as necessary for WS, skip the nested parallelism slide
Mention transpose and sorting and contrast their bounds
Note low depth is the important factor here. Cite by name
Show with example (sorting), which term is the dominant one? Qs or pdz?
What does Qp mean?
What does cache complexity mean for the running time?
-- for a greedy scheduler, the relation is “linear”
What we want
-- optimal work, Qs…

## Slide 27: PDF bound Paraphrased
For a program with sufficient available parallelism, we only need a slightly larger shared cache for P processors than for 1 processor.
P1
P1
M1
P2
P3
P4
M1
4d
Memory
Memory
4d
[Blelloch, G, Matias ‘99]
E.g., Matrix Multiply: MP = M1 + O(P log n)
Quicksort: Mp = M1 + O(P log2 n)

## Slide 28: Proof Sketch of Mp = M1 + P D result
Causes of additional cache misses
Both are cases of a executing “prematurely”
Read the same location
Out of order execution
a
b
Read the same location
Separated execution
a
b

## Slide 29: Premature Nodes
A node is premature at a point in the schedule if:
if it has been executed, and
there is a node with higher priority that has not yet been executed.
1
2
3
4
5
6
7
8
9
10
11
12
13
not yet executed
premature
mature

## Slide 30: Premature Node Lemma
PREMATURE NODE LEMMA [Blelloch, G, Matias ‘99]:
At any point during a prioritized schedule at most PD nodes are premature
Sufficient to bound extra memory to kPD if every node allocates at most k memory.
But note that:
Every premature node can cause an additional cache miss
Total number of premature nodes over time is not bounded by PD; it could be much larger

## Slide 31
Show that value will still be in cache for the delayed nodes (hold premature node’s value in extra cache space)
1
2
3
4
5
6
7
8
9
10
11
12
13
1
2
3
4
3
4
3
4
5
2
5
6
7
Sequential Order
Prioritized Parallel Order
Proof Sketch of Mp = M1 + P D result:
Basic Argument (case 1)

## Slide 32: Basic Argument (case 2)
…But still need to account for misses caused by executing a premature node itself
Show that for every additional miss caused by a premature node there is previous miss that becomes a hit
1
2
3
4
5
6
7
8
9
10
11
12
13
1
2
3
4
3
4
3
4
5
2
5
6
7
Sequential Order
Prioritized Parallel Order

## Slide 33: Case 2 sketch (by example)
Imagine reserving PD of cache just for premature nodes—moved to regular cache when they become mature.
As long as A has executed, but not node D, A is in the “special cache”
When A becomes mature, prioritize according to sequential order with respect to mature nodes
Will be there for E since we have M1 “regular cache” and any premature nodes go to the special cache
C
B
D
A
E

## Slide 34: Lecture 1 Outline
Multi-cores: today, future trends, challenges
Computations & Schedulers
    Modeling computations in work-depth framework
    Schedulers: Work Stealing & PDF
  Cache miss analysis on 2-level parallel hierarchy
    Private caches OR Shared cache
  Low-depth, cache-oblivious parallel algorithms
    Sorting & Graph algorithms

## Slide 35: Back to the Big Picture
Programmer writes high level parallel code
  Ideally, this is portable to different machines
A run time scheduler dynamically schedules program tasks on to the processors
Scheduler
Parallel program
Notes: Contrast with PEM, Valiant’s work
Bring Objective slide to next (push nested to later, delete
High level pic of par.comp. world.
Three components: computation, scheduler, machine
Programmers write high level code. Ideally he does not need to specify how it is to be run on a particular machine. it is mapped on to machines by schedulers
Machine is complex… f(sch, mach)
We want to construct a realistic model of machine, and construct provably good schedulers.

## Slide 36: Objective
Design portable parallel programs that can be scheduled to run fast on different kinds of machines
Memory
CPU
CPU
Shared Cache
CPU
Memory
CPU
CPU
CPU
Programmer should be able to obtain precise bounds based on certain metrics (like work, depth, cache/memory cost) of the program, and the choice of scheduler
Notes: Insert images – pr an shared cache images t
Measuring work, depth is standard. Need a model to measure memory cost

## Slide 37: Low-depth -> Good Cache Bounds
WS on Private caches:
    Only O(P D M1) more misses than sequential
  PDF on Shared cache:
    Mp = M1 + P D for no more misses than sequential
Important reason to have algorithm parallelism far exceed number of processors W/P + D (but still want D << W/P)

## Slide 38: Approach
Design a CO algorithm that:
is cache efficient under sequential execution
has low depth
(polylogarithmic)
For a parallel system,
use an appropriate scheduler that converts:
Good sequential cache complexity
To
Good parallel cache complexity
Good parallel
cache complexity
Notes: Next slide: plug in transpose and sortin in next slide, motivate good sorting
After that: Contributions slide instead of related work
Model, what to design, what results. New slide. Push related work to next slide to support the argument
r
Cite PEM paper, other related work

## Slide 39: Sequential Cache Complexity
Analysis: Bound the number of cache misses QA(n;M,B) of a sequential execution of
    Algorithm A on input of size n
    “ideal” cache of size M organized into
    blocks of size B
Cache Oblivious Algorithms
Algorithm A is designed w/o prior knowledge of cache or block size
Function QA is “smooth”
Number of cache misses is roughly QA on a realistic cache, same function for any number of cache levels
CPU
B
Main Memory
B
B
B
B
B
B
Ideal Cache Model [Frigo, Leiserson, Prokop, Ramachandran ’99]
size M
Notes: Describe the goal of the project
-- user thinks of data layout in general with out reference to a specific machine
-- user has a data layout that’s likely to wok well on most parallel machines
-- user should be able to analyse his design as well
Start with a description of dynamic parallelism
Talk about scheduling being behind the screen
For different machines, Schedulers do well on dags with property X (doing well = good parallel cache complexity on dynamic parallel dags)
-- define what seq and parallel cache complexity is
We design algos with property X
Describe M,B

## Slide 40: BT-Sort: [Blelloch, G, Simhadri ‘10] A poly-log depth, cache-oblivious sample sort
A (size n)
Let m=n1/2
A1
A2
A3
Am
m
m
S1 = Sort(A1)
S2 = Sort(A2)
S3 = Sort(A3)
Sm =Sort(Am)
m
A is a packed array of size n
Divide A into m rows & recursively sort each row to get S
Pick every log(n)th element from S (call this set X. |X| = n/log n)
Y = mergesort(X) Note: O(n/B) cache complexity
S
Notes: Comment on mergesort’s cache complexity.
Layout ??

## Slide 41: BT-Sort
A1
A2
A3
Am
m
m
S1 = Sort(A1)
S2 = Sort(A2)
S3 = Sort(A3)
Sm =Sort(Am)
m
m
S
Si
P
MERGE
4. Pick every (n1/2/log(n))th element from Y,
call this P (pivots). |P|= n1/2
5. Use CO merging algorithm (on (P, Si)) to partition each of Si into segments Sij (elements of Si that go to bucket j)
6. Can compute offset of each segment in bucket using CO prefix sum
A (size n)
Let m=n1/2
Notes: Comment on mergesort’s cache complexity.
Layout ??

## Slide 42: 7. Bucket Transpose
We know segment lengths & offsets - Can transfer in parallel
Each of the chunks might be very small compared to B. Cache miss overhead is high for naïve copying.
Our approach: D&C on the <row, bucket> index space
Invoke BKT-TRANSPOSE(1,1,n1/2) [Q(n;M,B) = only O(n/B)]
BKT-TRANSPOSE (x0, y0, size)
  IF size =1, just copy the one segment
  ELSE {BKT-TRANSPOSE (x0 , y0 , size/2); BKT-TRANSPOSE (x0 + size/2, y0 , size/2); two more recursive calls}
Send to
buckets
Notes: Slow down and talk about our solution?
when you make a call on an index space such that corresponding segments fit in cache, the index space contains (>B) arrays and buckets, the space wasted due to block boundaries is small (asymptotically) and the cache complexity of the call would be O(M/B), higher levels calls don’t access data and don’t count as additional misses
Critical path here, key insight: cutting index space can be shown to work through non-obvious analysis
Emphasize this slide as the key contribution
mention that the doing row or column major scans is a problem

## Slide 43: Sorting complexity
8. Finally, sort buckets
Q(n;M,B) = n1/2Q(n1/2;M,B)+ Q(xi;M,B) + O(n/B),
= O((n/B)(log(M/B)(n/B)).
Work(n) = O(n log n). Depth(n) = O(log2(n))
Depth of randomized version: O(log3/2(n))
[Cole, Ramachandran ’10] improves depth of deterministic sort to O(logn loglog n)
S1
S2
S3
Sm
Sort
Sort
Sort
Sort
Sort
Sort
Divide
using P
Send to
buckets
ANSWER
Notes: Improve latex
Show this outline upfront before and explain details further, and highlight layout
Cole, Vijaya’s new work (depth has been improved, ??open problem – log n depth )

## Slide 44: Sorting leads to graph algorithms
Problem | Depth | Cache complexity
List ranking | O(Dsort (n) log n) | O(Qsort (n))
Euler tour on trees (Successor + L.R.) | O(DLR(n)) | O(Qsort (n))
Tree contraction (Euler Tour + Indep. Set) | O(DLR(n) log n) | O(Qsort (n))
Least common ancestors (k queries) (Euler Tour + Range Minima Query) | O(DLR(n)) | O(⌈k/n⌉Qsort(n))
Connected components (Tree Contraction) | O(DLR(n) log n) | O(Qsort(¦E¦) log(¦V ¦/√M))
MST (Tree Contraction) | O(DLR(n) log n) | O(Qsort(¦E¦) log(¦V ¦/√M))
Notes: <talk about all these algorithms>
Comment on the complexities, which are optimal?

## Slide 45
 | weight | STL Sort | Sanders Sort | Quicksort | BT-Sort | BT-Sort
Cores |  | 1 | 32 | 32 | 32 | 1
Uniform | .1 | 15.8 | 1.06 | 4.22 | .82 | 20.2
Exponential | .1 | 10.8 | .79 | 2.49 | .53 | 13.8
Almost Sorted | .1 | 3.28 | 1.11 | 1.76 | .27 | 5.67
Trigram Strings | .2 | 58.2 | 4.63 | 8.6 | 1.05 | 30.8
Strings Permuted | .2 | 82.5 | 7.08 | 28.4 | 1.76 | 49.3
Structure | .3 | 17.6 | 2.03 | 6.73 | 1.18 | 26.7
Average |  | 36.4 | 3.24 | 10.3 | 1.08 | 28.0
Time in seconds on 32 core Nehalem (4 X x7560)
All inputs are 100,000,000 long
All code written run on Cilk++ (also tested in Cilk+)
BT-Sort follows Low-Span + Cache-Oblivious approach
BT-Sort: Experimental Study

## Slide 46: Multi-core Computing Lectures: Progress-to-date on Key Open Questions
How to formally model multi-core hierarchies?
What is the Algorithm Designer’s model?
What runtime task scheduler should be used?
What are the new algorithmic techniques?
How do the algorithms perform in practice?
NEXT UP
Lecture #2: Tackling Multi-level Hierarchies

## Slide 47: References
[Acar, Blelloch, Blumofe ‘02] Umut A. Acar, Guy E. Blelloch, Robert D. Blumofe. The Data Locality of Work Stealing. Theory Comput. Syst. 35:3 (2002)
[Blelloch, G ’04] G. E. Blelloch and P. B. Gibbons. Effectively Sharing a Cache Among Threads. ACM SPAA, 2004
[Blelloch, G, Matias ‘99] G. E. Blelloch, P. B. Gibbons and Y. Matias. Provably Efficient Scheduling for Languages with Fine-Grained Parallelism. J. ACM 46:2 (1999)
[Blelloch, G, Simhadri ‘10] G. E. Blelloch, P. B. Gibbons and H. V. Simhadri. Low Depth Cache-Oblivious Algorithms. ACM SPAA, 2010
[Blumofe, Leiserson '99] Robert D. Blumofe, Charles E. Leiserson. Scheduling Multithreaded Computations by Work Stealing. J. ACM 46:5 (1999)
[Blumofe et al. ’96] Robert D. Blumofe, Matteo Frigo, Christopher F. Joerg, Charles E. Leiserson, Keith H. Randall. An Analysis of Dag-Consistent Distributed Shared-Memory Algorithms. ACM SPAA, 1996
[Brent ‘74] Richard P. Brent. The parallel evaluation of general arithmetic expressions" J. ACM 21:2, 1974
[Cole, Ramachandran ’10] Richard Cole, Vijaya Ramachandran. Resource Oblivious Sorting on Multicores. ICALP, 2010
[Fortune, Wyllie ‘78] Steven Fortune, James Wyllie. Parallelism in Random Access Machines. ACM STOC, 1978
[Frigo, Leiserson, Prokop, Ramachandran ’99] Matteo Frigo, Charles E. Leiserson, Harald Prokop, Sridhar Ramachandran. Cache-Oblivious Algorithms. IEEE FOCS 1999
[Shiloach, Vishkin ‘82] Yossi Shiloach, Uzi Vishkin. An O(n² log n) Parallel MAX-FLOW Algorithm. J. Algorithms 3:2 (1982)